Accelerometer calibration certificate

Report # : {report_number}
Calibration Date : {calibration_date}
Next Calibration Date : {next_calibration_date}
Confidence level: {confidence_level}%

Calibrated By :
Certificate # :

Product details: / - Reference: {device_name} / - Manufacturer : Infinite Uptime / - MAC Address : {device_mac} / - Accelerometer details: / - Model name: {accel_name} / - Manufacturer: {accel_manufacturer} / - Range setting: {full_scale_range} / - Sensitivity: {accel_LSB}g	Calibrator details: / - Reference: {calibrator_name} / - Manufacturer: {calibrator_manufacturer} / - Calibrated on: {calibrator_calibration_date} / - Calibration certificate: {calibrator_certificate}

Technical note:
Purpose:
Infinite Uptime use the accelerometer raw measurements to compute a set of acceleration-derived physical quantities, that are the object of the current report.
For each of these physical quantities, confidence intervals are computed for a {confidence_level}% confidence level: to be certified, an Infinite Uptime device must deliver values for which the confidence interval must be within the [-{tolerance}%, +{tolerance}%] of the reference value.
Method:
For each of the physical quantities, and under predefined conditions, a sample of size N is polled and used to compute a confidence interval, expressed as a percentage of the calibrator reference value. Student’s t-distribution is used to find the critical value associated with N-1 degrees of liberty and the desired confidence level of {confidence_level}%.

Conditions	Physical Quantity	Reference Value	Mean	Standard Deviation	Confidence Interval	Result
Vibrations along Z axis: / - Temperature: 28°C / - Frequency: 80Hz / - Acceleration RMS: 1000mm/s2 / - Sample size: 10	Frequency (Hz)	80			[-3%, +3%]	OK
	Acceleration RMS on X axis (mm/s2)	0			[-5.2%, + 5.2%]	NOT OK
	Acceleration RMS on Y axis (mm/s2)	0
	Acceleration RMS on Z axis (mm/s2)	1000
	Velocity RMS on X axis (mm/s)	0
	Velocity RMS on Y axis (mm/s)	0
	Velocity RMS on z axis (mm/s)	2